## Slide 1: DPDK RTE_FLOW API Extensions for P4 Devices
Cristian Dumitrescu (Intel), Qi Zhang (Intel)

## Slide 2: Goal
Extend the DPDK RTE_FLOW API to support P4-programmable devices in a vendor-independent way. Some of these devices already have a DPDK driver, but no RTE_FLOW support.
  Intel ES2000 (link): Existing DPDK cpfl and idpf drivers.
  AMD Pensando DSC-200 (link): Existing DPDK ionic driver.
  Any other P4-programmable devices.
Initial “[RFC] ethdev: introduce generic flow item and action” sent on Aug 2, 2023: link.

## Slide 3: RTE_FLOW gaps for P4 devices
The current RTE_FLOW does not allow the users to define their own flow items and flow actions.
  The current RTE_FLOW only provides a predefined list of flow items and flow actions.
  For P4-programmable devices, the flow items (match key fields) and flow actions are defined by the user, without any knowledge or intervention from the vendor, through the P4 program.
Note: The goal is NOT to bypass the process of upstreaming new flow items and flow actions in the RTE_FLOW API; there is simply an infinite set of flow items and actions than can be defined by users in their P4 programs, and the vendor is completely unaware of them!

## Slide 4: Proposal 1 (RFC from Aug 2, 2023)
RTE_FLOW_ITEM_GENERIC
/** Matches a custom protocol header or metadata field represented as a byte array of a given length, whose meaning is typically defined by the data plane program.*/
struct rte_flow_item_generic {
uint32_t length; /**< Field length. */
const uint8_t *value; /**< Field value. */
};
/** Default mask for RTE_FLOW_ITEM_TYPE_GENERIC. */
static const struct rte_flow_item_generic rte_flow_item_generic_mask = {
.length = 0xffffffff,
.value = NULL,
};
RTE_FLOW_ACTION_GENERIC
/** Argument for the generic action. */
struct rte_flow_action_generic_argument {
uint32_t length; /**< Argument field length. */
const uint8_t *value; /** Argument field value. */
};
/** Generic action. */
struct rte_flow_action_generic {
uint32_t action_id; /**< Action ID. */
uint32_t action_args_num; /**< Number of action args. */
const struct rte_flow_action_generic_argument *action_args;
};

## Slide 5: Proposal 2 (Ori Kam)
Ori Kam (link): “Maybe we should add an API to register actions/items”.
int
rte_flow_item_register(uint16_t port_id,
int flow_item_id,
size_t flow_item_length,
const char *flow_item_description,
struct rte_flow_error *error);
struct rte_flow_action_argument {
size_t argument_length;
const char *argument_description;
};
int
rte_flow_action_register(uint16_t port_id,
int action_id,
uint32_t action_args_num,
const struct rte_flow_action_argument *action_args,
struct rte_flow_error *error);
Would this work?

## Slide 6: Proposal 3 (Ferruh Yigit)
Ferruh Yigit (link): “I suggest using a middle ground, instead of having wide open key/value based rte_flow item, rename it to RTE_FLOW_ITEM_TYPE_P4[SOMETHING], and have "struct rte_flow_item_p4[something]" to include all relevant fields to program a P4 pipeline, like table_id/table_name, value etc..”
Would this work?

## Slide 7: P4 program example
Complex P4 program example with user-defined flow items and flow actions: https://github.com/ipdk-io/networking-recipe/tree/main/p4src/linux_networking/dpdk